## Slide 1: WisDOT Aerial Imagery
2017 WisDOT Real Estate Conference
Cindy Mc Callum, Photogrammetry Unit Coordinator
Tiffany Novinska, Aerial Imaging Specialist
Surveying & Mapping Section, Photogrammetry Unit

## Slide 2: Introduction
Where is the Photogrammetry Unit within WisDOT?
  DTSD, Bureau of Technical Services, Surveying and Mapping Section
Who is the Photogrammetry Unit?
  Consists of 10 staff and 1 supervisor
    1 aerial imaging coordinator
    1 aerial imaging specialist
    1 photogrammetry coordinator/editor
    1.5 analytical triangulation specialists
    4.5 photogrammetry specialists
    1 LiDAR specialist

## Slide 3: Introduction
What is Photogrammetry?
The process of collecting precise elevation data and creating maps through the use of aerial imagery combined with surveyed ground control to achieve a vertical accuracy of 4 inches or better.
Why is Photogrammetry needed?
Provides engineering grade base mapping and elevation data for transportation improvement project planning and design.
How is Photogrammetry beneficial?
Allows coverage of a much larger area than conventional survey.
Aerial imagery is literally a snapshot in time of existing conditions which allows staff to return to the same point in time to gather additional data.

## Slide 4: Introduction
Cross-divisional partnership between DTIM and DTSD
  DTIM Aeronautics provides pilots for DTSD Photogrammetry aerial imagery flight missions.
Photogrammetry unit provides new, recent and historical aerial imagery to multiple areas within WisDOT including:
    DTSD – highways, facilities, environmental
      Requests originate from the Region Survey Coordinators
    DTIM – facilities, airports, rails
    OGC – court exhibits, historical review
    DSP – investigations, court exhibits, large event strategic planning

## Slide 5: Vertical aerial imagery
  Photograph taken looking straight down (nadir)
  High resolution film camera with in-house processing
  Black & White
  Scale varies depending on amount of area and detail needed
    Offered between 1”=250’ and 1”=2000’

## Slide 6: Vertical aerial imagery
  Film imagery is scanned into digital format at a high resolution
  Provided in .jpeg or .tif format
  High quality prints available as requested

## Slide 7: Flights are designed with 60% image overlap to provide stereo coverage for measuring elevation Portion of a 2015 mapping project: USH 12/14/18, Madison Beltline: Monona Dr. – CTH K
Controlled vertical aerial imagery flight plan

## Slide 8: Field survey
Field targeting
  Painted or plastic “X” or “T”
Ground control survey
  Latitude, longitude, height of targets are measured using GPS
Notes: The iron pin should be located in the center of the panel.

## Slide 9: WisDOT aerial imagery equipment
Camera system and aircraft:
Zeiss RMK TOP 15 Optical Film Camera
Cessna Turbo 210 Aircraft

## Slide 10
Typical scale is 1:3000, (1”=250’)
Each image covers approximately 0.18 square miles or 116 acres
Successive images are captured with 60% overlap
Flights require sunny and clear conditions
Spring leaf off conditions: after snow melts, before leaf out
  USH 14, Madison – Oregon
  Image date: 3/29/2016
  Scale: 1”=250’
  Altitude: 1500’ AGL
Controlled vertical aerial imagery

## Slide 11: Photogrammetry product uses:
  Planning and Scoping studies
  Base mapping for preliminary and final design
  Base mapping/DTM for current conditions for maintenance, slope studies and wetland mitigation sites
  Surface models
  Right of way plats
  Construction final quantities and payment
  Exhibits for reports and public meetings
  Public (open records) requests for aerial imagery
Notes: Most of our controlled vertical imagery is used to create mapping and DTM data for preliminary and final design, planning studies, right of way plats and exhibits.
We’ve also flown projects after construction to compute finals and after everything has been completed to show the existing conditions. This mapping can be used for traffic control plans, staged construction plans, resurfacing projects and for maintenance work. The DTM can be used for slope deficiency studies and beam guard projects.

## Slide 12
Photogrammetry product examples:
Planimetric mapping and digital terrain model
Orthoimagery – aerial image rectified to planimetric mapping and digital terrain model

## Slide 13
Planimetric Mapping
Discrete features: buildings, power poles, single trees
Relative features: culverts, tree lines
Beam guard: center of posts
Roads: level 11, e_rdwy
Shoulders: level 11, dashed, e_rdwy_gravel, e_rdwy_shldrpaved
Notes: Discrete features have accurate locations.
Buildings are compiled at the outside edge of the roofline, at the roofline elevation.
Power poles are measured on the ground, in the center of the pole.
Relative or representative features are roughly in their correct location and symbolized with generic cells such as culverts and tree lines .
The end of culverts are shown with an arc. A tree canopy is digitized at the average canopy height and shown with the tree line pattern.
The compilers measure the top of the posts of the beam guard. The pattern shows a line going through the posts which isn’t where the guard rail is actually located.
We usually collect the mapping and terrain data at the same time.
We can collect mapping only and deliver it and then collect the DTM data at a later date or not at all.
We fly some projects with very little ground control. These are called expedient planimetric. We won’t provide DTM data from these flights because of the lack of control.

## Slide 14
Photogrammetry product example:
Planimetric mapping used as part of a plan set

## Slide 15
Photogrammetry product example:
Planimetric mapping used for a Transportation Project Plat

## Slide 16: Aerial imagery archive (1937 – present)
Variety of areas covered throughout Wisconsin
  Most coverage is highway corridor specific
  Other areas may be available
  Research is required to determine availability
Scale depends on the original intent of the capture
Currently not all historic aerial imagery held by WisDOT is depicted in DOTView
  Please contact dotaerialimageryrequest@dot.wi.gov for assistance or call (608) 246-5397 or (608) 246-5392

## Slide 17: Aerial imagery archive (1937 – present) DOTView: http://dotnet/dotview/launch-dotview.htm (1975 - present)

## Slide 18: Aerial imagery archive example: USH 41/USH 45 Interchange, Winnebago County
4/24/1963
6/13/2014

## Slide 19: Aerial imagery archive example: Outdoor advertising sign issue, Rock County
2/16/1966
4/13/2006

## Slide 20: Oblique aerial imagery
  Captured at an angle to the surface of the earth
  Unscaled
  High resolution hand-held digital camera
  Provided in jpeg format via LAN or as discussed
  Hard copy prints available by request
  Imagery certification available by request

## Slide 21
08-22-2011
USH 41/STH 29 Interchange, Brown Co
Oblique aerial imagery:
documenting stages of highway construction
10-08-2013
11-05-2014

## Slide 22
STH 113, Merrimac Ferry Wayside improvements, 6-8-2016
Oblique aerial imagery:
Roadside facility documentation

## Slide 23
Moses Creek Wetland under construction, Stevens Point, 10-5-2010
Oblique aerial imagery:
Wetland monitoring

## Slide 24: How to request existing aerial imagery
Provide a map of the area required
Provide a range of years or decades of interest
What is needed?
  Vertical and/or oblique aerial imagery?
  Aerial imagery certification?
Send request via email to: dotaerialimageryrequest@dot.wi.gov
Call (608) 246-5397 or (608)246-5392

## Slide 25: Contact information
Cindy Mc Callum
Photogrammetry Unit Coordinator
Email: cynthia.mccallum@dot.wi.gov
Phone: (608) 246-7944
Tiffany Novinska
Aerial Imaging Specialist
Email: tiffany.novinska@dot.wi.gov
Phone: (608) 246-5397
DTSD, BTS, Surveying & Mapping Section
Photogrammetry Unit
3502 Kinsman Blvd
Madison WI 53704
FAX: (608) 245-8959

## Slide 26
Questions?
Thank you!