## Slide 1: Southeast Region Permit Submission
Greg Berry P.E.
February 2019

## Slide 2: Purpose
To provide requests to add information in permit request submittals to make processing more efficient
To review permits submittal requirements.

## Slide 3: Permit process Defined in HMM 9-15-15
  Permit Drawings:
    9-15-15
    2.3
    Each permit application shall contain adequate drawings showing the proposed location of the utility facility within the ROW with respect to the existing highway, any proposed highway improvement, and any existing utility facilities. The details shall include dimensions from the proposed utility installation to the commonly accepted ROW line and edge of the traveled way.
      Please show other existing utilities.
  2.4 Installation Information
    1. A general description of the location, size, type, nature, and extent of the utility facilities to be installed or to be adjusted, and the impact on the utility's existing facilities to remain in place within the ROW. This includes operating voltages for transmission lines, fiber counts, gas line pressures, etc.
    2. A description of proposed construction procedures, special traffic control and protection measures, erosion control measures, proposed access points, coordination of activities with the highway contractor, and trees/vegetation to be removed and replaced.

## Slide 4: Information requested on Submission Email
Please make sure Work Request or Project # is always in subject line of email. This is already almost always done, that is appreciated.
Include a note in the email that states the location; Municipality, County, and highway, and a close crossing road, so the location is easy to nail down.
Identify in the note The type ofr facility to be installed.
For Project permits:
  All of the above plus the WisDOT project number included in the subject line. Sometimes it is on the application, sometimes it is not.