## Slide 1: Utility Accommodation Policy & Permitting Updates
2018 Region Utility Conferences

## Slide 2: Today’s topics
2017 achievements: Permit form and UAP revised
Permit issuance
Work start and finish dates
Location maps
Permit drawings – what’s missing – what’s added
Pavement restoration
Don’t do this…
  Overhead line clearance
  Intersections and roundabouts
  Potholing
  Tree or vegetation cutting/spraying
  Casing

## Slide 3: Permit form revisions

## Slide 6
PREVIOUS

## Slide 7: Proposed indemnification
Similar to other state contracts HOLD HARMLESS: The permittee will indemnify and save harmless the State of Wisconsin and all of its officers, agents and employees from all suits, actions, or claims of any character brought for or on account of any injuries or damages received by any persons or property resulting from the operations of the permittee, or of any of its contractors, in prosecuting work under this permit.

## Slide 8




## Slide 9
CURRENT

## Slide 11: UAP – Revisions

## Slide 12: Overhead line clearance
UAP revised to aid overheight freight movement

## Slide 13: Overhead line clearance
HMM 09-15-25, Location Requirements
Special thanks to electric utilities for helping WisDOT to develop the proper NESC language

## Slide 18
NORTHEAST REGION

## Slide 19
SOUTHWEST
REGION

## Slide 20: Intersections and roundabouts
New language in HMM 09-15-25
I-41 @ 9th Ave, Oshkosh

## Slide 22: Permits involving tree or vegetation cutting/spraying

## Slide 23: Subsurface utility excavation Potholing HMM 09-15-45, Section 3.3

## Slide 24: Casing: HMM 09-15-45 Section 3.5
WisDOT does not require casing
WisDOT recommends casing:
  For facility protection
  To aid in future expansion
  To eliminate future boring costs
When casing is used, extend it at least:
  2 feet beyond the toe of slope
  3 feet beyond the ditch line
  2 feet beyond the curb in an urban section

## Slide 25: Permit Issuance: Maintaining Highway Authority
Wis. Stat. 86.07(2)(a) – Digging in highways…
WisDOT issues permits on state trunk highways (STHs)
Local governments issue permits on their highways
  Includes connecting highways
On STHs, potential problems with parking areas, terraces and sidewalks in municipalities
  Typically WisDOT does not maintain these areas

## Slide 29
WIS 67, Walworth

## Slide 32: Permit Issuance: Region v. Central Office (BHM)
Region offices issue most permits
Bureau of Highway Maintenance issues permits for:
  Expedited service connections (Not individual requests for service)
  The longitudinal occupation of interstates, freeways, and freeway/expressway mixes (hybrids) HMM 09-15-40
    Communications (including cellular), electric transmission
    20-year occupation fee involved
  All longitudinal installations of private utility facilities
  All installations not in conformance with, or exceptions to, the Utility Accommodation Policy
    These two items also require FHWA approval

## Slide 33: Work Start & Finish Dates

## Slide 35: Work Start and Finish Dates: Why are they important?
Issuance of other utility permits
Issuance of work on highway ROW permits
Planned or emergency maintenance work
Permanent Restoration
OSOW freight movement
Utility coordination: improvement projects
Calls from the public, businesses, press, etc.
WisDOT needs to know when you are working

## Slide 36
Includes permanent restoration. If the permitted work has not started by the “Work Finish Date”, this permit is null and void. If the permitted work has started, but has but has not bee completed by the “Work Finish Date”, the work shall not be completed unless authorized through an approved written time extension or a subsequent permit. ANY PERMIT ISSUED IS REVOCABLE


## Slide 37: Location maps

## Slide 38: County map from WisDOT website

## Slide 39: Plat map

## Slide 40: Municipal map

## Slide 43: HMM 09-15-15 Permit Drawings

## Slide 44: Provide dimensions from known points
Right-of-way line
Fence
Edge of pavement
Edge of travel lane
  White stripe
Centerline
Other utilities
Scale
Stationing
Section lines

## Slide 45: What’s missing with an application…
Erosion control plans
Traffic control plans
  Medium to larger projects
Environmental approvals, etc.
  DNR, ACOE correspondence, wetland maps
  Arch/Historical sites
  Tribal coordination
3-day notice sent to WisDOT
Appurtenances (not labeled, described, etc.)

## Slide 48: What may be added…

## Slide 49: Pavement Restoration
Need to do better – starts with the excavation
Pavement must be sawcut

## Slide 50
Don’t do this…

## Slide 51
HMM 09-15-45

## Slide 52
SDD 13C9

## Slide 54
Before
After

## Slide 55
Before
After

## Slide 56: Don’t do this…

## Slide 57: Don’t do this…

## Slide 58: PLEASE don’t do this…

## Slide 59: Central Office is moving…
My new address effective February 28: Bureau of Highway Maintenance 4822 Madison Yards Way, 5th Floor South Madison, WI 53705 - or - Bureau of Highway Maintenance
PO Box 7986
Madison, WI 53707-7986

## Slide 60: Where can WisDOT’s Utility Accommodation Policy be found?
http://wisconsindot.gov/Pages/doing-bus/real-estate/permits/utility-uap.aspx
Scan the QR code on the agenda

## Slide 61: Comments, questions, criticisms, concerns…
Bob Fasick
State ROW Permits Engineer
(608) 266-3438
robert.fasick@dot.wi.gov
This presentation is available at:
ftp://ftp.dot.wi.gov/dtsd/bhm/permits/utility/region-utility-confs/