## Slide 1: Material World
Leslie Ashauer, PE
NE Region Materials Engineer
2019 Northeast Region Construction Training
NWTC, Green Bay, WI
March 6, 2019

## Slide 2: Base Aggregates
Unique Identifier Number for Each Pit & Quarry
  Approved Products List → Aggregate Report
QMP Base Aggregates – SS 730
DON’T FORGET: Contact BAD IA with placement schedule

## Slide 3: Concrete Aggregate Testing
SS 701.3.3.2 QV Testing
  The department will conduct a minimum of 1 verification test for each 5 contractor QC tests unless specific QMP provisions specify otherwise.
Concrete Aggregate Testing: 1 QV per 5 QC
  Contractor tests aggregate during aggregate production
  QV will test aggregate during concrete production

## Slide 4: Concrete Class I
QV Test Result Notification – SS 715.3.1.3(2)
  Report to contractor within 2 business days of sampling

## Slide 5: Concrete Pavement
SS 715.2.3.1(6) SAM Number
  New mix designs need to include SAM number with mix design submittal.
SAM Testing
  QC required to test once per lot
  SAM test entered into MRS

## Slide 6: HMA Ignition Oven Correction Factor
1st Day of Production Sample
Mix Designs Prior to 12/1/2018
Provide to Region, Tested by BTS
Lab Batched Mix Sample
Mix Designs after 12/1/2018
Provide to Region 10 days prior to production

## Slide 7: Asphalt Content
Department Will Test Asphalt Content
  Acceptable content is within -0.3% of JMF
  AC more than -0.5% below JMF – contact PM, ME & HMA IA for resolution

## Slide 8: IRI Ride
SS 740
Provide As Much Notice As Possible – PLEASE!
Coordinate with Kim Heise

## Slide 9: Nulcear Density Testing
Test Duration & Gauge Placement

## Slide 10: Nuclear Density Random Numbers
Project Staff Determines Density Randoms
Provide QV Density Random Numbers to Appropriate IA

## Slide 11: Longitudinal Joint Density
Confined? Unconfined?
Notes: Pave Wider & Mill Out Later – Unconfined
No Cost to the Department (milling and extra material)
Qty of Extra Material is Calculated
Test at location according to CL NOT, the unconfined edge

## Slide 12: MRS Entry
Contractor Must Enter ALL Contractual Tests
  Structures
  Pavement
  PCC Thickness
  HMA
  IRI Ride
  Soils & Aggregates

## Slide 13: Documentation
NEW 2019 Process
Material Archive
  Material documentation retained in long-term storage for future reference
Materials Project Records
  Material documentation to be retained with the construction project records

## Slide 14: Proposed CMM 8-45 Table
Material User Group is updating CMM 8-45 and applicable sections to define the new department process for material finals.

## Slide 15: E-Guide
Committee Rewriting ALL E-Guides
  Anticipated end of March for update
  Follow proposed documentation process

## Slide 16: Certification of Materials – DT1310
Rewrite of CMM 8-45: May 2019
  Non-Conforming Materials
  Non-Performance of QMP (QC & QV)
  Buy America Exemption
  2019 Construction: DISINCENTIVES

## Slide 17: Non-Performance / Nonconformance
Credit Consistency
Credits ≥ $5,000
  Reviewed by Region / BPD / BTS
Credits < $5,000
  Reviewed by Region
Notes: 33 Columns of information to enter

## Slide 18: Credit Consistency
Submit Log of Credits Annually
Review for Commonalities
  Contractor
  Tester
  Spec Issues

## Slide 19: Pantry
Online