## Slide 1
BIM for Bridges and Structures Pilot Project Updates – Utah DOT
Mark Daniels
UDOT Structures Design Manager

## Slide 2: Presentation Outline
Goals
Recent Experience
Design
Bid Letting
Construction
What’s Next?
Notes:   Objectives and Goals
  We have learned that his delivery method impacts to project delivery processes and how we do business
Recent Experience: 2 Pilot projects under construction4 bridge structures (3 replacements, 1 new)
Design Learning curve, software is changing rapidly, create a standard process that needs to be adaptable as software improves. Each project is different as the technology is changing – need to constantly adapt
Bid Letting--> Interesting nuances
Construction 1st bridge essentially complete

## Slide 3: Digital Delivery Goals
    Produce a more optimal design
    Improve information transfer
    Obtain and manage better data to improve decision making
    Improve efficiency
Notes:     UDOT’s Overarching Program is coined Digital Delivery
    Produce a more optimal design
  Clash Detection, utilities, better visualization with terrain
    Improve information transfer
  Provide better-defined quantities
  Reduce risk on both the Contractor and Owner side
  The contractor knows what is included in project
    Obtain and manage better data to improve decision making
  Prevent rework from project to project
  Collect asset management information
    Improve efficiency
  Minimize the recreation of data
    Ideally data is housed in one location over the life of the bridge i.e. collecting all info to manage more efficiently
  Improve procedures and processes
    Improve workflows to reduce overlap and unnecessary work – reduce re-work i.e. cutsheets

## Slide 4: BIM for Bridges and Structures Recent Experience
    I-80 over UPRR at Blackrock
Notes: Have done several roadway projects, Blackrock is the first UDOT Digital Bridge Project.
Blackrock is currently under construction
CMGC Delivery Method, Contractor Granite Construction, gives benefit of contractors knowledge and needs
I-80 EB/WB Full Replacement of each structure, Michael Baker International
SR-36 Replacement includes a new alignment, HDR provided design services and construction support

## Slide 5: BIM for Bridges and Structures Recent Experience
    I-80 over UPRR at Blackrock
Notes: Existing Structure:
3-span pre-stressed girder
Carries I-80, lots of freight, important route
Over UPRR
Deck in very poor condition, major repairs in the past with significant traffic impacts
Pin and hanger detail on frequent inspection schedule. Also has a steel bent diaphragms-not common in our inventory
During CMGC looked at sliding a new structure in place but ultimately decided to use an Acrow temporary bridge

## Slide 6: BIM for Bridges and Structures Recent Experience
Notes: View from above
Located just south of Great Salt Lake

## Slide 7: BIM for Bridges and Structures Recent Experience

## Slide 8: BIM for Bridges and Structures Recent Experience
Notes: Detailed model view showing retaining walls and other features.
Existing bin walls in poor condition needed replacement.
One of the complicated aspects of this project is construction of the retaining walls in relation to the phasing of the structure and tight constraints with UPRR ROW.
(T-walls were used for the retaining walls-Precast Modular Retaining Wall system (concrete facing units))
Model was used in project meetings to facilitate discussion.

## Slide 9: BIM for Bridges and Structures Recent Experience
    SR-36 over I-80
Notes: Also part of the Blackrock project is SR-36 over I-80.
These are pictures and plans for the original structure which is a 4 span steel girder bridge.
Deck has had issues for several years now.
The construction of this bridge is essentially complete. Will highlight it in more detail later on in presentation.

## Slide 10: BIM for Bridges and Structures Recent Experience
    5600 West Over UPRR
Notes: 5600 West over UPRR is our second endeavor in Digital Delivery. Michael Baker International is Designer and Construction Support. HDR is reviewer
Delivery method is design bid build.
Design is complete.
Ready to advertise, were planning on being in construction by now. However, coordination with RR is ongoing. (Hoped to be in construction right now)

## Slide 11: BIM for Bridges and Structures Recent Experience
    5600 West Over UPRR
Notes: The 5600 West RR crossing is currently an at grade crossing.
The new structure over the RR will accommodate the current RR lines as well as future lines for an intermodal hub.
Structure will be a multi-span pre-stressed concrete girder.

## Slide 12: BIM for Bridges and Structures Design
Notes: Took a plan sheet and went through with the Contractor to determine what information they needed.
This helped us distinguish between information that we want and need and distinguished it from what the contractor needs
Traditional delivery vs. Digital Delivery
Green – Needed information. i.e. remove existing structure Convey in model or by some other means
Yellow – include in the model i.e. material properties, dimensions
Red – Not needed by Contractor (Design information, i.e. load ratings etc.), moved all notes to General notes sheet

## Slide 13: BIM for Bridges and Structures Design
Notes: Went through a discovery process to determine how information would be conveyed.
Attachment, shown geometrically, or data
First shot at setting standards.

## Slide 14: BIM for Bridges and Structures Design
    Model Development
    Solids Model Creation
    Reinforcing Steel Detailing
    Publish Model
    Application of Attributes to Elements
Notes: Model development thought of as a four step process.
Solids model creation, detailing, applying attributes, and publishing the model.
Will go a little more in detail on these items in the next few slides.

## Slide 15: BIM for Bridges and Structures Design
    Solids Model Creation
Notes: This was done in Bentley OBM
Build geometry of bridge by 3D solid elements
Modify elements to ensure correct geometry as designed
Elements have no intelligence other than basic shape and size

## Slide 16: BIM for Bridges and Structures Design
    Reinforcing Steel Detailing
Notes: Use Solids model as guidelines for reinforcement location
Apply reinforcement or any additional detailing such as welds and bolt patterns to detail model (ProStructures).
Elements are similar to solids model elements (no intelligence)

## Slide 17: BIM for Bridges and Structures Design
Application of Attributes to Model
Notes: Apply attributes and attachments to solids and detail model
Includes all information that would not be included in the basic geometry of the solids and detailing model. (Mark numbers, material properties, screed elevations, specifications, etc.)
Create and attach any reports that are created from the solids and detail model

## Slide 18: BIM for Bridges and Structures Design
Publish Models for Review and Construction
Notes: Publish or export models that will be used for review and construction models
Ideally all design information and geometry for all disciplines are included in one model.

## Slide 19: BIM for Bridges and Structures Design
Notes: Rendering created by HDR

## Slide 20: BIM for Bridges and Structures Design
QC/QA
    Output Reports
    Verification Checklists
    Acceptance
    Reviews
Notes: QC/QA is much different than before.
Will discuss these 4 items…

## Slide 21: BIM for Bridges and Structures Design
Output Reports
Notes: Output reports from software are very convenient (sometimes difficult to manipulate)
Elevation Reports
Quantity Reports
Geometry Reports
Reinforcement Bending Schedules
Attributes Applied to Model

## Slide 22: BIM for Bridges and Structures Design
Verification Checklists
Notes: Verification lists were created for checking
Models and output reports were checked.

## Slide 23: BIM for Bridges and Structures Design
Reviews
Notes: Bluebeam for attachments (detail sheets). Liked Bluebeam since comment form can be manipulated to display like out standard comment form.
Experimented with Navigator
Usual Excel form was used for other model comments (this is how we typically make comments).

## Slide 24: BIM for Bridges and Structures Design
Acceptance
Notes: Detailed description of what is contractual and what is FIO.
Description of which stamp applies to which portion of the model.
“Special Considerations”. We did not change project schedule to accommodate this delivery method. They had to figure out work arounds. Not a research project. This problem will change as software changes.

## Slide 25: BIM for Bridges and Structures Design
Design Challenges
Notes: Workspace
Software-Temperamental, instable, new versions sometimes not compatible. Assurances that things are improving.
Attachments-information didn’t always attach or transfer to the imodel
Lots of attachments are shown in this model. The designers have found a more effective wat to attach things to the model.

## Slide 26: BIM for Bridges and Structures Bid Letting
Notes: Had opportunities for contractors to view models as design progressed (before bidding).
Pre Bid Meetings are important.
Clear description of where information is found.

## Slide 27: BIM for Bridges and Structures Construction
Notes: Had to define workflows for design advertising, Preconstruction, Construction, Closeout
The Digital Delivery Method changes everything. One of the first tasks for the CMGC was to figure out how that was going to go

## Slide 28: BIM for Bridges and Structures Construction
Notes: Important to think about who needs what information, and how information is conveyed.
For example, how are Shop Drawing Submittals handled?

## Slide 29: BIM for Bridges and Structures Construction
Training
Notes: Weekly training Meetings during construction-Very helpful Plan on paying for this item.
Training personnel on how to use the model to obtain information.
I observed the following from some of the meetings….
Would do a 3-week look ahead to make sure everyone was familiar with how to obtain information on specific tasks.
The surveyors are the ones who seem to enjoy this delivery method the most, previously they would have to create their own models in Trimble, now they can just export it.
What equipment did you have to buy? Already had most of it, used Trimble Business Center for years (due to using on roadway projects), already had rovers, had to buy some tablets.
What subs used it? It was mainly reinforcing steel supplier that benefited. Used ifc files to create shop drawings for review. Not really used by structural steel supplier or precaster.
Very helpful for visualization.
Some loved it, some didn’t.
Started using Navigator, but some switched to Bentley Viewer after it came out. Different people liked different software.
Difficulty orienting self in model, had designers place a McDonalds sign to orient themselves.
Appreciated different saved views, with all levels on Model is overwhelming.
Plans read like a book, models don’t.
Need uniformity between designers.

## Slide 30: BIM for Bridges and Structures Construction
Inspection
Notes: How are they using it on the bridge, surveying more, traditional methods to verify.
Some like it, some don’t
Inspectors had difficulty because they were used to a system of marking up and tabbing plan sheets.
Liked it for checking elevations.
Variety of tablets, ios vs android

## Slide 31: BIM for Bridges and Structures Construction

## Slide 32: BIM for Bridges and Structures Construction

## Slide 33: BIM for Bridges and Structures Construction

## Slide 34: BIM for Bridges and Structures Construction

## Slide 35: BIM for Bridges and Structures Construction
As-Constructed
Notes: From May 2019

## Slide 36: BIM for Bridges and Structures Construction
Construction Challenges
Notes: Software and Hardware
Extracting Information from the model-measuring
Verification Documentation
Changes to the model, how to distribute and keep track of versions

## Slide 37: BIM for Bridges and Structures What’s Next?
Capture Project Lessons Learned
Develop Project Delivery Manual for Digital Delivery
Partner with Software Developers
Review Contract Terms and Conditions
Next Project…
Notes: Project manual for digital deliver
Guidance and manuals
Standards
90th South to Redwood Rd. Widening

## Slide 38
Thank You