## Slide 1
Eric Christie, PE
Deputy State Maintenance Engineer, ALDOT
Robert J. Taylor, PE
United States Sales, CESTEL
“The Portable Bridge WIM”

## Slide 2
Agenda
Alabama
2018 Lift Axle Study
Mississippi
2018 Harvest Study
2016 Enforcement

## Slide 3
2006 FHWA SCAN Tour, Slovenia
Notes: George Conner, Assistant Director, was instrumental in bringing the product back to the US from the FHWA funded 2006 SCAN Tour.
ALDOT currently owns one SiWIM system at a permanent location. ALDOT has also contracted with CESTEL to monitor and collect data at additional sites in 2017 and 2018.

## Slide 4
FHWA SCAN Tour Slovenia
2018 Alabama Lift Axle Study
Notes: I will overview the 2018 study.
Reason for study………….
Apart from using smaller wheels on lift axles, numerous drivers did not deploy the lift axle at all during transportation of heavy loads.
Fully loaded 1-S-3 rigid truck with one axle lifted, 82,700 pounds (legal limit 60,000 pounds).

## Slide 5
2018 Alabama Lift Axle Study
Notes: ALDOT, State Troopers and Cestel found 4 locations where based on their close proximity to industry where trucks with lift axles are utilized. A major focus of the project was to perform measurements to determine the presence of 1-S-3 (4-axle) trucks with lift axles and their appropriate utilization of those lift axles.

## Slide 6
2018 Alabama Lift Axle Study
Notes: If didn’t take us long to begin scratching our heads.
There are several types of lift axles with most of them performing as they are designed, however, during the measurements several vehicles were detected using smaller wheels on the lift axles. The above axle does not perform as expected and carries only 1,000 to 3,000 pounds instead of an expected 10,000 lbs.

## Slide 7
2018 Alabama Lift Axle Study
Notes: Above shows a 6-axle vehicle with slightly over 87,000 pounds with a lift axle deployed. The lift axle was carrying only 500 pounds.
Apart from using smaller wheels on lift axles, numerous drivers did not deploy the lift axle at all during transportation of heavy loads.

## Slide 8
Lift Axle Utilization Loaded & Unloaded
2018 Alabama Lift Axle Study
Notes: An analysis was made for all 1-S-3 trucks with lift axles.
Lift Axle Down: The 1-S-3 vehicle was considered to be overloaded if GVW was over 75,000 pounds.
Lift Axle Up: The 1-S-3 vehicle was considered to be overloaded if GVW was over 60,000 pounds.
This slide indicates we have loading issues in Alabama. It doesn’t appear that the lift axle allowance has helped.

## Slide 9
Overloading on US-31 Autauga County
2018 Alabama Lift Axle Study
Notes: Looking specifically at the US-31 site in Autauga County.
We see 51.9% of trucks with lift axle down were still overloaded.
We also see 69.7% of trucks with lift axle up were overloaded.
Oddly, this our permanent SiWIM location that is often used for enforcement.

## Slide 10
Incremental GVW overloading on 1-S-3 trucks with lift axle up (US-80 Montgomery County)
2018 Alabama Lift Axle Study
Notes: We then analyzed 1-S-3 trucks with lift axles up, that were overloaded (gross vehicle weight over 60,000 pounds) on the US-80 Montgomery County site which had the most overloaded trucks. Figure 55 depicts those trucks in 2,000 pounds increments.

## Slide 11
Incremental GVW overloading on 4-axle trucks (US-80 Montgomery County)
2018 Alabama Lift Axle Study

## Slide 12
GVW overloading on 1-S-3 trucks with lift axle down (US-80 Macon County) 50% Min. Loading
2018 Alabama Lift Axle Study
Notes: The 50% minimum loading issue was then analyzed. The 1-S-3 vehicles with lift axle down and with at least one 20,000 lb. axle within a group were analyzed. This was done by comparing the minimum and maximum axle weight of the group. In the following figures, the ratio between the lightest and the heaviest axle within the group is presented in percentage groups.
126 of 674 were in compliance = 19% This may be due to a lack of understanding of the law.

## Slide 13
2018 Alabama Lift Axle Study
Notes: Here enforcement is being conducted at the US-31 Autauga County site where the BWIM is located.
The live feed allows enforcement to screen.

## Slide 14
Monday – December 5, 2016 (2:55PM)
2018 Alabama Lift Axle Study

## Slide 15
ALDOT Summary
115,412 lbs
2018 Alabama Lift Axle Study
Notes: As the Bridge maintenance Engineer, I see the results of overloading on a weekly basis. I oversee 8? enforcement crews continually weighing trucks at locations all over Alabama. Standing alongside our enforcement crews, I have seen gross violations and I have see law abiding drivers trying to stay within the law.
BWIM and our in-pavement systems allow us great analytics. The main utility for BWIM for us is for analysis of locations where it is unfeasible for a in place system. We can have a BWIM up and running in a day or two and usually there is no need for traffic control.

## Slide 16
2018 Mississippi Harvest Study
Notes: Reason for study………….
According to the project guidelines, two appropriate locations for SiWIM measurements were determined in the Mississippi Delta. The locations were selected after discussions with enforcement officers in the region followed by inspections of potential bridges in the area. The bridges were selected due to their proximity to major grain bins where crops are delivered. Shown are locations of those Grain Silos (blue trucks) and selected locations (yellow pins). Special thanks to Chief Huff and his officers for their assistance in selecting optimal locations.

## Slide 17
2018 Mississippi Harvest Study
Vehicle Distribution Daily Average
Notes: A time analysis was then performed focusing on all vehicles and their distribution over time. The time histograms presented shows the distribution of the traffic over the 31 days of traffic. A significant number of harvest trucks with gross vehicle weight over 90,000 pounds were detected. Some of the vehicles have significantly overloaded tandem axles with weights exceeding 27,000 pounds per axle
As expected, the heavier traffic is in lane #2 headed in the direction of the silo (upper graph).
Also, we see an average work day in the bottom 2 charts (lower graph).

## Slide 18
2018 Mississippi Harvest Study
SR-8 Asymmetrical Overloading & Overloaded Breakdown
Notes: Asymmetrical overloading per lane, where lane 2, which carries mostly loaded crop trucks is heavily overloaded.

## Slide 19
2018 Mississippi Harvest Study
SR-8 5-axle semi-trailer 84,000 pounds during the measurement

## Slide 20
2018 Mississippi Harvest Study
SR-6 Heaviest Crop Truck
Notes: The heaviest truck on SR-8 was similar at 121,165 lbs. The record holders on both measurement sites were drivers, which managed to load their vehicles over 120,000 pounds, more than 40% over legal limit (see Figure 25 and Figure 26). Most of the overloaded log trucks were detected during early morning. Individual axles were overloaded to 27,000 pounds.

## Slide 21
2018 Mississippi Harvest Study
Tractor with trailer weighing 157,982 pounds

## Slide 22
2016 Mississippi Enforcement
Notes: Reason for study………….

## Slide 23
2016 Mississippi Enforcement

## Slide 24
2016 Mississippi Enforcement
Optimal Enforcement Times

## Slide 25
2016 Mississippi Enforcement
Notes: Figure 22: Heaviest lumber truck, detected during measurement, 133,512 pounds

## Slide 26
“Questions”
Eric Christie, PE
Deputy State Maintenance Engineer, ALDOT
Robert J. Taylor, PE
United States Sales, CESTEL

## Slide 27
2018 Mississippi Enforcement

## Slide 28
2018 New Jersey Bridge Analysis
I-195 Mercer County, NJ
Notes: The South Bound Direction had a large depression in the asphalt near the bridge end slab. While this was not ideal for traffic analysis (bouncing), it was suitable for bridge analysis.
The North Bound Direction had recently been resurfaced which provided a smooth transition onto the bridge and very good conditions for traffic analysis.

## Slide 29
2018 New Jersey Bridge Analysis
31 Days of Traffic
Notes: Presented on Figure 11 is 31 days of traffic on measured section, where measured days are applied on X-axis and gross vehicle weight in kips is applied on the Y-axis. Change in density of traffic can be observed, regarding the time of day (i.e. much less traffic during the night and during the weekend). Also, July 4th significant drop in vehicle count can be observed. It was not uncommon to detect vehicles with gross vehicle weights over 100 kips (36 vehicles during the period of 314 days).

## Slide 30
2018 New Jersey Bridge Analysis
Comparison between 20kips and 22.4kips axle load limit
Notes: By using common limit of 20,000 pounds per axle, overloading per axle become more significant, almost 2/3 of all overloaded vehicles, as shown in Figure 15. With lower axle load limit all vehicles, that were previously only GVW overloaded, become also axle overloaded.

## Slide 31
SiWIM Attributes
Economical.
Portable - One system can be used at multiple locations.
System installed in 1 day.
Traffic stream unaware & no impact to pavement.
Very good accuracy.
Data collection at locations unaffordable prior to BWIM.
Data collection made easy.

## Slide 32
Date Utility
Bridge Design & Bridge Maintenance.
Asset Management.
Enforcement.
State Planning.
Roadway Design & Roadway Maintenance.

## Slide 33
Data Utility-Asset Management
Axle and Gross Vehicle Weight
Axle Spacing and Gross Vehicle Length
Classification
Speed
Time/Date/Bridge Stamp
Photo

## Slide 34
Data Utility-Enforcement

## Slide 35
Pre-Selection for Enforcement

## Slide 36
Pre-Selection for Enforcement

## Slide 37: Pre-Selection for Enforcement

## Slide 38
Monday-December 5, 2016
2:55 PM
SiWIM App

## Slide 39
Data Utility-Enforcement
Notes: This is our full capability.

## Slide 40
Data Utility-State Planning
Notes: Increased data.
Freight planning. Freight routes.

## Slide 41
Data Utility-Roadway Design & Maintenance
Accurate Counts & Loading
Asphalt Spreader Photo
Notes: WIM Portability makes accurate counts and loading affordable on any route.

## Slide 42
Data Utility - Bridge Design & Maintenance
Notes: Posting.
Structural analysis/influence lines.

## Slide 43
Data Utility - Bridge Design & Maintenance
Notes: Posting.
Structural analysis/influence lines.

## Slide 44
SiWIM® System Installation and Calibration

## Slide 45
Select a Route/Bridge
I-195 Hamilton NJ
July 2017
Installation
Notes: two bridges on I-195 over Klockner Road between Yardville and Bordentown in Mercer County. The purpose of the measurements was to perform 1-month measurements at two separate bridges. The measurements were used for 1)traffic analysis and to compare results with existing pavement WIM site just west of the bridge and 2)bridge analysis.
Both measurement locations were operational 100% of the time with reliable detection of over 99% of all heavy vehicles with gross vehicle weight over 7,000 pounds.
Measurements took place beginning on June 24th and ended on July 24th 2017 and 54,139 commercial vehicles were detected and processed. (31 Days)

## Slide 46
Installation
Notes: Partial road block.
Hamilton Police Department
Off the peak traffic hours.

## Slide 47
Installation

## Slide 48
Installation
Notes: The leading and trailing sensors (blue) provide distance between axles and velocity of the vehicle.
Other sensors (red) provide GVW and IAL.

## Slide 49
ST-503 Strain transducer
Installation

## Slide 50
Installation
Notes: Installation: Wednesday, June 21st and Thursday, June 22nd..
Calibration: Monday, June 26th.
Sensors: 16 sensors were used per bridge.

## Slide 51
Installation
Notes: Files are post-processed with the SiWIM-D software package, which among others:
Searches for outliers (doubtful results),
Reclassifies vehicles, if necessary,
Counts single, double, triple and other axles,

## Slide 52
Calibration
Notes: Traffic Stream
Pre-weighed and measured vehicle.

## Slide 53
A Mississippi Story

## Slide 54
Metrics - MDOT North Bridge

## Slide 55
Metrics - MDOT North Bridge

## Slide 56
Metrics - MDOT North Bridge

## Slide 57
Metrics - MDOT North Bridge

## Slide 58
Metrics - MDOT North Bridge

## Slide 59
Exceptional Transport (NJ)
Notes: Exceptional transport
SiWIM system was also used for monitoring exceptional transports, where type of the vehicle, its GVW and axle loads, as well as compliance with permit can be inspected, like speed limit over the bridge, time of day and other specifics.
The record holder was exceptional transport with gross vehicle weight of 195,620 pounds (Figure 19).

## Slide 60
2018 New Jersey Bridge Analysis
I-195 Mercer County, NJ
Notes: The South Bound Direction had a large depression in the asphalt near the bridge end slab. While this was not ideal for traffic analysis (bouncing), it was suitable for bridge analysis.
The North Bound Direction had recently been resurfaced which provided a smooth transition onto the bridge and very good conditions for traffic analysis.

## Slide 61
2018 New Jersey Bridge Analysis
31 Days of Traffic
Notes: Presented on Figure 11 is 31 days of traffic on measured section, where measured days are applied on X-axis and gross vehicle weight in kips is applied on the Y-axis. Change in density of traffic can be observed, regarding the time of day (i.e. much less traffic during the night and during the weekend). Also, July 4th significant drop in vehicle count can be observed. It was not uncommon to detect vehicles with gross vehicle weights over 100 kips (36 vehicles during the period of 314 days).

## Slide 62
2018 New Jersey Bridge Analysis
Comparison between 20kips and 22.4kips axle load limit
Notes: By using common limit of 20,000 pounds per axle, overloading per axle become more significant, almost 2/3 of all overloaded vehicles, as shown in Figure 15. With lower axle load limit all vehicles, that were previously only GVW overloaded, become also axle overloaded.

## Slide 64
SiWIM Attributes
Economical.
Portable - One system can be used at multiple locations.
System installed in 1 day.
Traffic stream unaware & no impact to pavement.
Very good accuracy.
Data collection at locations unaffordable prior to BWIM.
Data collection made easy.

## Slide 65
Date Utility
Bridge Design & Bridge Maintenance.
Asset Management.
Enforcement.
State Planning.
Roadway Design & Roadway Maintenance.

## Slide 66
Data Utility-Asset Management
Axle and Gross Vehicle Weight
Axle Spacing and Gross Vehicle Length
Classification
Speed
Time/Date/Bridge Stamp
Photo

## Slide 67
Data Utility-Enforcement

## Slide 68
Pre-Selection for Enforcement

## Slide 69
Pre-Selection for Enforcement

## Slide 70: Pre-Selection for Enforcement

## Slide 71
Monday-December 5, 2016
2:55 PM
SiWIM App

## Slide 72
Data Utility-Enforcement
Notes: This is our full capability.

## Slide 73
Data Utility-State Planning
Notes: Increased data.
Freight planning. Freight routes.

## Slide 74
Data Utility-Roadway Design & Maintenance
Accurate Counts & Loading
Asphalt Spreader Photo
Notes: WIM Portability makes accurate counts and loading affordable on any route.

## Slide 75
Data Utility - Bridge Design & Maintenance
Notes: Posting.
Structural analysis/influence lines.

## Slide 76
Data Utility - Bridge Design & Maintenance
Notes: Posting.
Structural analysis/influence lines.

## Slide 77
SiWIM® System Installation and Calibration

## Slide 78
Select a Route/Bridge
I-195 Hamilton NJ
July 2017
Installation
Notes: two bridges on I-195 over Klockner Road between Yardville and Bordentown in Mercer County. The purpose of the measurements was to perform 1-month measurements at two separate bridges. The measurements were used for 1)traffic analysis and to compare results with existing pavement WIM site just west of the bridge and 2)bridge analysis.
Both measurement locations were operational 100% of the time with reliable detection of over 99% of all heavy vehicles with gross vehicle weight over 7,000 pounds.
Measurements took place beginning on June 24th and ended on July 24th 2017 and 54,139 commercial vehicles were detected and processed. (31 Days)

## Slide 79
Installation
Notes: Partial road block.
Hamilton Police Department
Off the peak traffic hours.

## Slide 80
Installation

## Slide 81
Installation
Notes: The leading and trailing sensors (blue) provide distance between axles and velocity of the vehicle.
Other sensors (red) provide GVW and IAL.

## Slide 82
ST-503 Strain transducer
Installation

## Slide 83
Installation
Notes: Installation: Wednesday, June 21st and Thursday, June 22nd..
Calibration: Monday, June 26th.
Sensors: 16 sensors were used per bridge.

## Slide 84
Installation
Notes: Files are post-processed with the SiWIM-D software package, which among others:
Searches for outliers (doubtful results),
Reclassifies vehicles, if necessary,
Counts single, double, triple and other axles,

## Slide 85
Calibration
Notes: Traffic Stream
Pre-weighed and measured vehicle.

## Slide 86
A Mississippi Story

## Slide 87
Metrics - MDOT North Bridge

## Slide 88
Metrics - MDOT North Bridge

## Slide 89
Metrics - MDOT North Bridge

## Slide 90
Metrics - MDOT North Bridge

## Slide 91
Metrics - MDOT North Bridge

## Slide 92
Exceptional Transport (NJ)
Notes: Exceptional transport
SiWIM system was also used for monitoring exceptional transports, where type of the vehicle, its GVW and axle loads, as well as compliance with permit can be inspected, like speed limit over the bridge, time of day and other specifics.
The record holder was exceptional transport with gross vehicle weight of 195,620 pounds (Figure 19).

## Slide 93
Portable WIM – Why?
Economical.
Portable - One system can be used at multiple locations.
System installed in 1 day.
Traffic stream unaware & no impact to pavement.
Very good accuracy.