## Slide 1: OSHA Occupational Health and Safety Administration
Interim Enforcement Guidance for the Respirable Crystalline Silica in Construction Standard, 29 CFR 1926.1153

## Slide 2: New Silica Exposure Rules
Enforcement date September 23, 2017 – Applied to Construction
  Requires employers to use engineering and work practice controls to reduce and maintain employee exposures to respirable crystalline silica to or below the permissible exposure limit (PEL), unless the employer can demonstrate that such controls are not feasible.
  Where controls are not sufficient to reduce employee exposure to or below the PEL, the employer must:
    Use controls to reduce employee exposure to the lowest feasible level and supplement them with the use of respiratory protection.
https://www.osha.gov/dsg/topics/silicacrystalline/

## Slide 3: What is Silica?
Crystalline silica is a common mineral found in materials like sand, stone, concrete, and mortar.
Respirable crystalline silica – very small particles at least 100 times smaller than ordinary sand – is created when cutting, sawing, grinding, drilling, and crushing stone, rock, concrete, brick, block, and mortar.

## Slide 4: Why is Respirable Silica a problem?
Workers who inhale these very small crystalline silica particles are at increased risk of developing serious silica-related diseases, including:
  Silicosis, an incurable lung disease that can lead to disability and death;
  Lung cancer;
  Chronic obstructive pulmonary disease (COPD); and
  Kidney disease.

## Slide 5: How does this change my role?
The OSHA rule was intended for the individuals/employees engaged in the task or assisting with the task that creates exposure to respirable crystalline silica.
  As an example OSHA states employees directing traffic nearby are not engaged in the task are not required to have respirators.
Consultants should read and understand the OSHA guidance. Consultants must make sure their employees are educated and protected.

## Slide 6: Protect yourself
If possible avoid being in close proximity to the task.
If unavoidable use a respirator.
If you think you will need a respirator, request one.
For in-house staff respirators are located in the supply cabinet by the Traffic Section.
Read the guidance and understand ways to reduce your exposure.