## Slide 1: OSHA Occupational Health and Safety Administration
Interim Enforcement Guidance for the Respirable Crystalline Silica in Construction Standard, 29 CFR 1926.1153

## Slide 2: New Silica Exposure Rules
Enforcement date September 23, 2017 – Applied to Construction
  Requires employers to use engineering and work practice controls to reduce and maintain employee exposures to respirable crystalline silica to or below the permissible exposure limit (PEL), unless the employer can demonstrate that such controls are not feasible.
  Where controls are not sufficient to reduce employee exposure to or below the PEL, the employer must:
    Use controls to reduce employee exposure to the lowest feasible level and supplement them with the use of respiratory protection.
https://www.osha.gov/dsg/topics/silicacrystalline/

## Slide 3: What is Scilica?
Crystalline silica is a common mineral found in materials like sand, stone, concrete, and mortar.
Respirable crystalline silica – very small particles at least 100 times smaller than ordinary sand – is created when cutting, sawing, grinding, drilling, and crushing stone, rock, concrete, brick, block, and mortar.

## Slide 4: Why is Respirable Silica a problem?
Workers who inhale these very small crystalline silica particles are at increased risk of developing serious silica-related diseases, including:
  Silicosis, an incurable lung disease that can lead to disability and death;
  Lung cancer;
  Chronic obstructive pulmonary disease (COPD); and
  Kidney disease.

## Slide 5: How does this change my role?
The OSHA rule was written with the employees engaged in the tasks or assisting with the task listed.
  As and example OSHA states employees directing traffic nearby are not engaged in the task are not required to have respirators.
  Questions that have not been answered :
    Is there a recommended safe distance from the operation for people to avoid the silica dust cloud?
    How long is the silica airborne?
WisDOT is developing a safety directive for our employees addressing Respirable Silica (In progress). Silica was discussed in our annual field safety training.
Consultants need to read and understand the enforcement guidance. Consultants must make sure their employees are educated and protected.

## Slide 6: What you should see in the field
Contractors may use water or vacuums to control dust during operations that would cut, drill, saw, grind or crush stone, brick, mortar, concrete.
If contractor staff is using respirators, should you be too?

## Slide 7: Protect yourself
WisDOT is working on developing guidance for complying with the order.
If you think you need a respirator, request one.
Read the guidance and understand ways to reduce your exposure.