## Slide 1: I-39/90 and County N interchange
Open House
Stoughton Senior Center
December 6, 2017

## Slide 2
Outline of topics
I-39/90 construction schedule in 2017
  County N interchange schedule
  Interstate expansion near interchange
What is a modern roundabout?
Why roundabouts?
County N interchange roundabouts
Public education
Questions

## Slide 3
2017 construction schedule
Three bridge replacements over I-39/90:
  County AB bridge, south of Madison
  Manogue Road bridge, near the rest area north of Janesville
  Stateline Road bridge, near Beloit
Reconstruction of the I-39/90 and County N interchange (Exit 147), and Interstate expansion in this area.
Temporary widening of I-39/90 southbound:
  Between County AB and East Church Road, north of the US 51 interchange (Exit 156).
  From the I-39/90 and County S (Shopiere Road) interchange (Exit 183) to the Illinois state line.
Reconstruction and expansion of I-39/90 northbound:
  From the Dane/Rock County line to East Church Road, northeast of Stoughton.
  From Hart Road near Beloit north to the I-39/90 and US 14 interchange in Janesville.
I-39/90 northbound near the WIS 73/US 51 interchange in Edgerton

## Slide 4
Began construction in late April 2017.
Interchange ramps to remain open during construction, besides periodic nighttime ramp closures.
County N, between I-39/90 and Rinden Road, closed from early May to Friday (December 8, 2017).
  Signed detour: I-39/90, US 12/18 and County N.
Interchange roundabouts to opened in early November 2017.
Interchange complete on Dec. 12, 2017.
County N interchange schedule
Note: Dates are weather dependent and subject to change.

## Slide 5
Construction: fall 2017 – fall 2018
Two lanes to remain open on I-39/90, especially during peak travel times.
  Nighttime lane closures expected 8 p.m. to 5 a.m. M-F.
Be alert for traffic shifts and crossovers in this area.
Interchange ramps to remain open during construction, besides periodic nighttime ramp closures.
Interstate expansion near County N
Note: Dates are weather dependent and subject to change.

## Slide 6: What is a modern roundabout?

## Slide 7
What is a modern roundabout?
Compact circular intersection
Traffic flows counter-clockwise around a center island
Entering traffic yields
Channelized approaches to deflect traffic and reduce entry speeds

## Slide 8
“Typical” 4 way intersection

## Slide 9
Slight circular movement

## Slide 10
Not to be confused with…
Rotary
Traffic Circle
Traffic Calming Circle

## Slide 11
Signing & Marking
Proper signing and marking help drivers anticipate the roundabout

## Slide 12: Why roundabouts?

## Slide 13
Roundabout benefits
Higher-capacity
Suitable for high and low-flow intersections
Aesthetics – landscaping/civic feature
Safest type of at-grade intersection
  Angle of conflict
  Slower speeds
  Simplified decision-making

## Slide 14
Safety comparison
Conventional intersection vs. roundabout
Crossing conflicts eliminated with roundabout

## Slide 15
Safety comparison
Traffic signal vs. roundabout
Traffic Signal | Roundabout
High speeds | Low speed
Wide visual scans | Narrow visual scans
Less time to react | More time to react
High severity crashes | Low severity crashes

## Slide 16
National studies
32%
Total crashes
Convert two-way stop intersection to roundabout
71%
Fatal/injury crashes
21%
Total crashes
Convert signalized intersection to roundabout
66%
Fatal/injury crashes
Notes: New HSM data

## Slide 17
Chart: 
Column1 | 0.15 | 0.45 | 0.85
Pedestrian injury probability
Pedestrian’s chance of death if hit by a motor vehicle
Source: Oregon DOT, Dept. of Transport (UK)

## Slide 18
Wisconsin Roundabout Crash Study
Studied 56 Wisconsin roundabouts to their ‘no build’ intersection control:
  Yield, Stop, Signalized
Results:
  Increase in total number of crashes—mostly ‘fender benders’
  40% reduction in fatal and serious injury crashes
  Consistent trends with several other states

## Slide 19: I-39/90 & County N interchange
Notes: View looking south

## Slide 20
Why roundabouts at the County N interchange?
Intersection Control Evaluation
Control options evaluated
  Stop, conventional diamond
  Traffic signal:
    Conventional diamond
    Diverging diamond
  Roundabout, conventional diamond
Similar impacts, costs, operations
Traffic Signals
  Not expected to meet warrants (southbound ramp)
Roundabouts
  Safety advantage, better operations
Roundabouts were ultimately chosen
Notes: Costs w/in 6% of each other (740K between high and low: DDI>roundabout>signal>stop)
SB ramp meets warrants in 2031 (outside of 5 yr construction window)

## Slide 21: How to drive roundabouts

## Slide 22
What should I NOT do?

## Slide 23
What should I NOT do?
Failure to yield, improper lane changes

## Slide 24
Yielding
OK to enter the roundabout

## Slide 25
Yielding
Not OK to enter
Waited for a safe gap



## Slide 26
Large vehicles – Truck apron
Where trucks are common, a properly designed apron may be necessary

## Slide 27
Large vehicles
2015 WI law requires motorists to yield the right-of-way to larger vehicles:
  40-ft (or more) in total length
  10-ft wide
When in doubt, give ‘em room

## Slide 28
Entered in right lane…
…trailer drifts into left lane when circulating
Large vehicles
Notes: Truck will switch lanes entering to circulating

## Slide 29
Entering


Notes: Stay out of the “no zone”
https://youtu.be/p0rp7szsgfw

## Slide 30
Circulating


Notes: Stay out of the “no zone”

## Slide 31
Emergency vehicles

## Slide 32
  Stay informed and involved!
Register for project email updates at www.i39-90.wi.gov.

## Slide 33: Questions?
www.i39-90.wi.gov
i39-90Project@dot.wi.gov
Facebook.com/WisconsinI3990Project
(608) 884-1234

## Slide 35
BP
Road Ranger

## Slide 36
Landscaping
Not just for aesthetic purposes
Speeds are slower, yield rates are higher when sight is restricted
Notes: Old IIHS data

## Slide 37
National Study
44%
All crashes
87%
Fatal/injury crashes in rural area
Fatal/injury crashes in urban area
78%
72%
1-lane
2-lane
Convert two-way stop intersection to roundabout
Notes: Old IIHS data

## Slide 38
Public education