## Slide 1: 2019 Material Reminders

## Slide 2: TSS Contacts
Anne Wallace
  Materials Supervisor
Travis Mikshowsky
  Soils and Materials Engineer
Jeanette Frazer
  IA Specialist
Steve Ames
  HMA Specialist
Scott Willinger
  Railroad/Materials Specialist
Bill Kobleska
  Lab Coordinator

## Slide 3: 2019 Material Reminders

## Slide 4: 2019 Material Reminders
Passing Stockpile Test for Aggregates Prior to Placement for Both QC and QV
Stockpile sampling should be a coordinated effort between QC and QV (Standard Spec 730)

## Slide 5: 2019 Material Reminders
Passing Stockpile Test for Aggregates Prior to Placement for Both QC and QV
Stockpile sampling should be a coordinated effort between QC and QV (Standard Spec 730)
QMP Base Aggregate is now in the Standard Specs (Section 730)
Passing Stockpile test prior to placement
  *If either the QC or QV stockpile test fails, Both the QC and QV will resample side by side and rerun the tests
Pay Reduction Table now in the Spec
Definitions/Extents for Non-Conforming Material
Stockpile tests are valid for multiple projects for up to 60 days from day stockpile test was taken
A lot of other changes

## Slide 6: 2019 Material Reminders
Passing Stockpile Test for Aggregates Prior to Placement for Both QC and QV
Stockpile sampling should be a coordinated effort between QC and QV (Standard Spec 730)
Check That All the Aggregates Being Used Are From A Source That is Approved For the Aggregate’s Intended Use

## Slide 7: 2019 Material Reminders
Notify Materials Section Two days prior to placement of:
HMA
Base Aggregate
Concrete
Check That All the Aggregates Being Used Are From A Source That is Approved For the Aggregate’s Intended Use
Passing Stockpile Test for Aggregates Prior to Placement for Both QC and QV
Stockpile sampling should be a coordinated effort between QC and QV (Standard Spec 730)

## Slide 8: 2019 Material Reminders
Notify Materials Section Two days prior to placement of:
HMA
Base Aggregate
Concrete
Check That All the Aggregates Being Used Are From A Source That is Approved For the Aggregate’s Intended Use
Passing Stockpile Test for Aggregates Prior to Placement for Both QC and QV
Stockpile sampling should be a coordinated effort between QC and QV (Standard Spec 730)
Aggregate Minimum Sample Size

## Slide 9: 2019 Material Reminders
Fill out Non-Conformance/Non-Performance Spreadsheet as Issues Come Up
Materials Section will Request in October 2019
Notify Materials Section Two days prior to placement of:
HMA
Base Aggregate
Concrete
Check That All the Aggregates Being Used Are From A Source That is Approved For the Aggregate’s Intended Use
Passing Stockpile Test for Aggregates Prior to Placement for Both QC and QV
Stockpile sampling should be a coordinated effort between QC and QV (Standard Spec 730)
Aggregate Minimum Sample Size

## Slide 10: 2019 Material Reminders
Fill out Non-Conformance/Non-Performance Spreadsheet as Issues Come Up
Materials Section will Request in October 2019
SWIG 8-45 For Materials Information
Notify Materials Section Two days prior to placement of:
HMA
Base Aggregate
Concrete
Check That All the Aggregates Being Used Are From A Source That is Approved For the Aggregate’s Intended Use
Passing Stockpile Test for Aggregates Prior to Placement for Both QC and QV
Stockpile sampling should be a coordinated effort between QC and QV (Standard Spec 730)
Aggregate Minimum Sample Size

## Slide 11: 2019 Material Reminders
Fill out Non-Conformance/Non-Performance Spreadsheet as Issues Come Up
Materials Section will Request in October 2019
SWIG 8-45 For Materials Information
Notify Materials Section Two days prior to placement of:
HMA
Base Aggregate
Concrete
Check That All the Aggregates Being Used Are From A Source That is Approved For the Aggregate’s Intended Use
*There are Plenty of Changes to All Materials so Check the Standard Spec, ASP 6, and CMM (Or You Can Always Call a Materials Team Member)
Passing Stockpile Test for Aggregates Prior to Placement for Both QC and QV
Stockpile sampling should be a coordinated effort between QC and QV (Standard Spec 730)
Aggregate Minimum Sample Size

## Slide 12: Other Material Reminders
Field Reviews
  Notify Materials Staff when
  Benchmarks are achieved
  Larger Projects
  30% Reviews
  60% Reviews
  Smaller Projects
  50% Review

## Slide 13: Other Material Reminders Concrete
Optimized Gradation for Concrete Pavements
  This SPV should be on every concrete paving project that requires slip form paving
  This SPV doesn’t require the use of an optimized gradation but gives contractors the option
  Can be added through a No Cost Change Order with no incentives if not in contract this year

## Slide 14: Other Material Reminders Concrete
Super Air Meter (SAM)
  Now required with concrete pavement through 715.3.1.1 (2)
  Exceptions for small quantities, HES, SHES, and approach slabs
  Contractor is required to run test and enter it into the MRS for information only

## Slide 15: Other Material Reminders Concrete
Super Air Meter Air Meter

## Slide 16: Other Material Reminders Concrete
  What is different about the Super Air Meter?

## Slide 17: Other Material Reminders Concrete
New QV testing frequency for concrete pavement (715.3.1.3 (1))
  1 QV tests for every 5 QC with at least 1 QV test per lot
  Example
    4 Lots with 8 QC tests/Lot = 32 QC Tests
    Will need 7 QV tests with at least one in each lot
  Example
    6 Lots with 4 QC tests/lot = 24 QC Tests
    Will need 6 QV tests to get one in each lot

## Slide 18: Upcoming HMA Training
  Part 1 – Two Online HMA Training through the LearnCenter
    1) Type “AASHTO TC3 HMA Paving Field Inspection” into the search bar
    2) Also available April 1st will be an online 2019 PWL Training

## Slide 19: Upcoming HMA Training
  Part 2 – March 7th in La Crosse
    More in depth HMA classroom training that will cover:
      Review of the online trainings
      HMA Basics
      PWL
      SMA
      Longitudinal Joint Density
      Tack Coat
      Lab testing
      Etc.
      *Lab open house after the training for demonstrations on HMA testing practices

## Slide 20: Questions?